## Slide 1
ML Surrogates for Agent-Based Transport Models
Uncertainty Quantification for GNN-Based Traffic Prediction
Thesis Defence Presentation
Supervisors: Dominik Natterer | Elena
Paris MATSim Dataset • 1,000 Scenarios • 31,635 Road Segments
March 2026

## Slide 2
The Problem
Why do we need an ML surrogate?
2
Technical University of Munich | Chair of Urban Transport Systems
2
Fig: 1. Overall thesis pipeline: MATSim simulations → GNN surrogate → uncertainty-guided decisions
Without Surrogate
• 1 MATSim scenario = 8+ hours
• Policy testing = weeks of compute
• Very few alternatives evaluated
With GNN Surrogate
• 1 scenario = seconds
• BUT: needs uncertainty estimates
• When can we trust the output?

## Slide 3
4 Research Questions
3
Technical University of Munich | Chair of Urban Transport Systems
3
RQ1
MC Dropout Effectiveness
How well does MC Dropout capture epistemic uncertainty in GNN traffic surrogates? (measured by Spearman ρ between predicted σ and actual error)
RQ2
MC Dropout vs Ensembles
How does MC Dropout compare to ensemble-based UQ in terms of uncertainty quality and computational efficiency?
RQ3
Combining Identical Models
Does combining uncertainty from architecturally identical models help? What role does diversity play?
RQ4
Distribution-Free Coverage
Can conformal prediction & temperature scaling transform raw uncertainty into trustworthy intervals with formal coverage guarantees?

## Slide 4
Dataset & Experimental Setup
Paris MATSim Road Network
4
Technical University of Munich | Chair of Urban Transport Systems
4
Fig: 2. Paris road network as directed graph. Coral nodes = capacity-reduced segments. Each node = one road segment. Target: Δv = volume change (veh/h).
Road segments (nodes)
31,635
Network edges
~85,000
Scenarios used
1,000 (10% of 10,000)
Training scenarios
800
Validation scenarios
100 (T7-T8)
Test scenarios
100 (T7-T8)
Total test predictions
3,163,500
GPU
NVIDIA T4 (Colab)
5 Input Features per node:
• VOL_BASE_CASE • CAPACITY_BASE_CASE
• CAPACITY_REDUCTION • FREESPEED • LENGTH

## Slide 5
GNN Architecture: PointNetTransfGAT
6-layer graph neural network for node-level regression
5
Technical University of Munich | Chair of Urban Transport Systems
5
Fig: 3. PointNetTransfGAT: PointNetConv (geometry) → TransformerConv (attention) → GATConv (output). Input: 5 features per node. Output: Δv per node (veh/h).
Stage 1
PointNetConv-1
Start-point geometry encoding [5 → 512]
Stage 2
PointNetConv-2
End-point geometry encoding [512 → 128]
Stage 3
TransformerConv-1
4-head attention [128 → 256]
Stage 4
TransformerConv-2
4-head attention [256 → 512]
Stage 5
GATConv
Neighbourhood aggregation [512 → 64]
Stage 6
GATConv (final)
Scalar prediction (T2-T8) [64 → 1]
Dropout applied in PointNetConv & TransformerConv layers

## Slide 6
8 Training Trials: Performance Summary
Best model = T8 (R² = 0.5957)
6
Technical University of Munich | Chair of Urban Transport Systems
6
Fig: 4. R², MAE, RMSE across Trials 2–8. T8 achieves best R²=0.5957, MAE=3.96 veh/h among UQ-compatible trials.
Trial
R²
MAE
Dropout
UQ?
T1
0.786
2.97
0.0
❌
T2
0.512
4.33
0.3
partial
T3
0.225
5.99
0.0
❌
T4
0.243
6.08
0.0
❌
T5
0.555
4.24
0.3
✓
T6
0.522
4.32
0.3
✓
T7
0.547
4.06
0.3
✓
T8★
0.596
3.96
0.2
✓ Best
T1 excluded from UQ: zero dropout → σ=0 everywhere

## Slide 7
Why T1 is Excluded & T9 Failed
Understanding the boundaries of our UQ approach
7
Technical University of Munich | Chair of Urban Transport Systems
7
Fig: 5. Trial progression T1→T8: R² (top) and MAE (bottom). T8 = best UQ-compatible trial.
T1 — Excluded from UQ
• Has highest R² = 0.786 and MAE = 2.97
• BUT: effective dropout = 0.0
• All S=30 passes give identical output
• σ = 0 everywhere → UQ undefined
• Architectural constraint, not a flaw
T9 — Heteroscedastic (Negative Result)
• Tried: predict mean AND variance directly
• Result: R² = 0.02 (target was ≥ 0.57)
• Model inflated variance to absorb errors
• Instead of improving mean predictions
• Known failure mode (Seitzer et al.)

## Slide 8
6 UQ Methods Evaluated
All post-hoc — no model retraining required
8
Technical University of Munich | Chair of Urban Transport Systems
8
1
MC Dropout
S=30 stochastic passes at inference time
2
Ensemble Variance
5 seeded runs, std of per-run means
3
Combined UQ
√(σ²_MC + σ²_ens) quadrature sum
4
Conformal Pred.
Distribution-free coverage guarantee
5
Selective Pred.
Filter by σ threshold, keep confident ones
6
Temp. Scaling
Post-hoc calibration with scalar T

## Slide 9
RQ1: What is MC Dropout?
Keeping dropout active at inference to estimate uncertainty
9
Technical University of Munich | Chair of Urban Transport Systems
9
Fig: 6. S=30 stochastic forward passes through T8. Per-node mean (ŷ) and std (σ) computed. σ serves as the uncertainty estimate. Spearman ρ=0.4820.
Step 1
Load trained model with dropout layers
Step 2
Enable dropout at inference time
Step 3
Run S=30 forward passes on same graph
Step 4
Compute per-node mean: μ = (1/S)Σŷₛ
Step 5
Compute per-node std: σ = std(ŷ₁...ŷ₃₀)
Step 6
High σ = model uncertain about this road
S=30 chosen: plateau reached at S≈25, S=50 gives only +1% ρ

## Slide 10
RQ1 Results: MC Dropout Uncertainty Quality
T8 achieves ρ = 0.4820 — best among all UQ-compatible trials
10
Technical University of Munich | Chair of Urban Transport Systems
10
Fig: 7. Per-graph Spearman ρ across all 100 test scenarios. Mean=0.464, Std=0.023 — consistent quality, no outlier scenarios.
Trial
Dropout
Test Graphs
Spearman ρ
T5
0.3
50
0.4263
T6
0.3
50
0.4186
T7
0.3
100
0.4460
T8★
0.2
100
0.4820
ρ = 0.4820
Uncertainty-Error Correlation
AUROC = 0.76
Error Detection (top-10% errors)
ΔR² = −0.010
Accuracy Cost of Enabling Dropout

## Slide 11
S = 30 Convergence Analysis
Choosing the right number of MC forward passes
11
Technical University of Munich | Chair of Urban Transport Systems
11
Fig: 8. Spearman ρ vs number of MC samples S (T8, 10 test graphs). Both ρ and mean σ plateau at S≈25. Circled point = S=30 (chosen operating point).
Why S=30?
Convergence plateau:
• ρ flattens sharply after S≈25
• S=30 → ρ = 0.4584
• S=50 → ρ = 0.4632 (+1.0% only)
Compute cost:
• S=30: 228 min on T4 GPU
• S=50: ~380 min (+67% cost)
• Gain: only +1% improvement
Conclusion:
S=30 is on the plateau.
Optimal cost-quality trade-off.

## Slide 12
RQ2: MC Dropout vs Ensemble Variance (Exp A)
5 seeded runs on same T8 model
12
Technical University of Munich | Chair of Urban Transport Systems
12
Fig: 9. Spearman ρ for all evaluated UQ methods. MC Dropout (blue) outperforms ensemble variance (orange). Best = Exp A Combined (ρ=0.4909).
Experiment A Results
MC Dropout (S=30)
ρ = 0.4908
Ensemble Variance
ρ = 0.4370
Combined (MC+Ens)
ρ = 0.4909
Key Finding
• MC Dropout beats Ensemble Variance by +12.3%
• Combined adds negligible benefit (+0.01 ρ)
• Ensemble variance is largely redundant
Note: PyTorch Geometric API bug fixed before evaluation

## Slide 13
RQ3: Multi-Model Ensemble (Exp B)
T2 + T5 + T6 + T7 + T8 — weighted by individual R²
13
Technical University of Munich | Chair of Urban Transport Systems
13
Fig: 10. Comprehensive UQ comparison: T7 vs T8 across AUROC, Spearman ρ, k₉₅, MAE, and selective prediction.
Experiment B: 5-Model Ensemble
Ensemble ρ
0.4333
Ensemble R²
0.5656
Best single (T8) R²
0.5957
MC Dropout ρ (T8)
0.4908
Why ensemble doesn't help accuracy
• Models span R² 0.51 (T2) to 0.60 (T8)
• Averaging weaker models dilutes T8
• Architectural diversity not tested here
• UQ-wise: ρ=0.4333 < MC Dropout 0.4908

## Slide 14
Technical Finding: PyTorch Geometric API Bug
Why ensemble results had to be corrected
14
Technical University of Munich | Chair of Urban Transport Systems
14
Problem: Silent GATConv weight mismatch
Original ensemble scripts loaded checkpoints with strict=False. PyG 2.3.1 expected lin_src.weight / lin_dst.weight, but checkpoints stored lin.weight (older format). Weights silently dropped → R² dropped from ~0.59 to near-zero.
Before Fix (Corrupted)
Ensemble R²: ~0.0
Ensemble ρ: ~0.0
After Fix (Corrected)
Ensemble R²: 0.5656
Ensemble ρ: 0.4333
Fix: Remapped checkpoint keys before loading with strict=True
Impact: MC Dropout, conformal prediction, temperature scaling results are NOT affected — they used the matching PyG version.

## Slide 15
RQ4: The Calibration Problem
Raw MC Dropout σ is NOT a calibrated standard deviation
15
Technical University of Munich | Chair of Urban Transport Systems
15
Fig: 11. Scaling factor k₉₅ needed for ±kσ to achieve 95% coverage. Ideal Gaussian: k=1.96. T8 MC Dropout requires k=11.34 — nearly 6× larger.
Fig: 12. Reliability diagram (left): observed coverage always below diagonal = systematic under-coverage. ECE = 0.265 means coverage deviates 26.5 pp on average.
Key insight: σ is a ranking signal — NOT a probability. Spearman ρ=0.4820 works perfectly. But ±1.96σ only gives 54.8% coverage (target: 95%).

## Slide 16
RQ4: Coverage — MC Dropout vs Conformal
Conformal prediction fixes the coverage gap
16
Technical University of Munich | Chair of Urban Transport Systems
16
Fig: 13. T8 calibration curve. Raw MC Dropout (blue) severely undercovers. Global conformal (orange) and adaptive conformal (green) both hit nominal targets.
Coverage Comparison Table
Nominal
Raw MC Coverage
Conformal Coverage
50%
23.3%
50.0%
80%
40.1%
80.0%
90%
48.6%
90.0%
95%
54.8%
95.0%
Why conformal works
• Uses empirical calibration quantile
• Distribution-free — no assumptions
• Guaranteed by construction
• Cost: wider fixed intervals

## Slide 17
RQ4: Temperature Scaling — Post-Hoc Calibration
Single scalar T=2.70 reduces ECE by 82%
17
Technical University of Munich | Chair of Urban Transport Systems
17
Fig: 14. Top: reliability diagrams before (ECE=0.269) and after (ECE=0.048) scaling with T=2.70. Bottom: coverage gap reduction at each nominal level. Evaluated on 80 held-out graphs.
What is Temperature Scaling?
σ_scaled = σ_raw × T Optimal T learned on calibration set (20 graphs) by minimising ECE.
T = 2.70
Optimal scaling factor
ECE: 0.265 → 0.048
82% improvement
NLL: 21.65 → 4.75
78% improvement
KS stat: 0.245 → 0.104
PIT improvement
95% coverage: 83.3%
Not 95% — residual gap
Useful middle step. Residual gap at tails → conformal prediction still needed for guarantees.

## Slide 18
RQ4: Split Conformal Prediction
Distribution-free coverage guarantee — no model assumptions needed
18
Technical University of Munich | Chair of Urban Transport Systems
18
Fig: 15. Conformal prediction workflow for T8. 100 test graphs → 50 calibration + 50 evaluation. Calibration residuals define quantile q. Intervals ŷ±q guarantee ≥90% or ≥95% coverage.
How It Works
1
Split test data: 50 calibration + 50 evaluation graphs
2
On calibration set: compute residuals |y − ŷ| per node
3
Find quantile q at desired level (e.g. 90th or 95th)
4
Apply to eval set: interval = [ŷ − q, ŷ + q]
5
Coverage guaranteed: ≥90% or ≥95% by construction
Key: Guarantee holds regardless of model internals
Only assumption: data is exchangeable

## Slide 19
RQ4: Conformal Prediction Results
Near-exact coverage achieved at both levels
19
Technical University of Munich | Chair of Urban Transport Systems
19
Fig: 16. Nominal vs achieved coverage (left) and interval half-widths (right). Both 90% and 95% levels meet targets within 0.02 percentage points. Evaluated on 50 graphs (1,581,750 nodes).
Coverage Results (T8)
90% level
q = 9.92 veh/h
Achieved: 90.02%
95% level
q = 14.68 veh/h
Achieved: 95.01%
What this means for planners
• At least 95% of true Δv values fall within ±14.68 veh/h
• This guarantee is mathematically proven
• Fixed-width: same interval for every road segment
• Cost: ~6× wider than raw MC Dropout interval

## Slide 20
RQ4: Adaptive Conformal Prediction
Combining MC Dropout ranking with conformal guarantees
20
Technical University of Munich | Chair of Urban Transport Systems
20
Fig: 17. Left: standard conformal over-covers low-uncertainty nodes (98.6%) and under-covers high-uncertainty (62.9%). Right: adaptive conformal narrows this to [90.0%, 96.2%] — much more uniform conditional coverage.
Standard vs Adaptive
Standard conformal:
• Fixed width ±q for all nodes
• D1 (low σ): 98.6% coverage
• D10 (high σ): 62.9% coverage
Adaptive conformal:
• Width = q_adapt × σ (node-specific)
• Wider where model is uncertain
• Narrows disparity → [90%, 96.2%]
Best of both worlds:
MC Dropout σ provides adaptive widths. Conformal guarantees marginal coverage.

## Slide 21
Selective Prediction: Filter by Uncertainty
Keep only confident predictions → dramatically lower MAE
21
Technical University of Munich | Chair of Urban Transport Systems
21
Fig: 18. MAE as fraction of retained predictions (sorted by ascending σ) for T8. Retaining the 50% most certain predictions gives −41.2% MAE. Based on 100 test graphs (3,163,500 nodes).
Retained
MAE (veh/h)
Reduction
100%
3.95
—
90%
3.23
−18.3%
50%
2.32
−41.2%
25%
1.79
−54.6%
10%
1.06
−73.3%
Practical use for planners
Accept bottom 50% σ → expect MAE ≈ 2.32 veh/h
Run full MATSim only for top 10% most uncertain

## Slide 22
The 3-Layer UQ Hierarchy
Main practical recommendation of this thesis
22
Technical University of Munich | Chair of Urban Transport Systems
22
LAYER 1
MC Dropout (S=30)
Purpose: RANKING predictions by reliability
• σ = per-node uncertainty estimate
• Spearman ρ = 0.4820 with actual error
• AUROC = 0.76 for error detection
• Use: selective prediction, flagging
LAYER 2
Temperature Scaling (T=2.70)
Purpose: CALIBRATE σ toward probability
• σ_scaled = σ_raw × 2.70
• ECE reduced 82% (0.265 → 0.048)
• Better Gaussian approximation
• Use: when approximate probabilities needed
LAYER 3
Conformal Prediction
Purpose: GUARANTEE coverage bounds
• 90.02% at 90% nominal ✓
• 95.01% at 95% nominal ✓
• Distribution-free — no assumptions
• Use: contractual / operational requirements
→
→
All three methods are post-hoc: no model retraining required. They can be applied to any trained GNN.

## Slide 23
UQ Methods: Summary Comparison
All 5 methods evaluated on T8 (100 test graphs, 3.16M predictions)
23
Technical University of Munich | Chair of Urban Transport Systems
23
Method
Key Metric
Strength
Limitation
MC Dropout (S=30)
ρ=0.4820 CRPS/MAE=0.857
Node-specific ranking Selective pred. −41.2% MAE
Not calibrated (k₉₅=11.34) S-fold compute cost
MC Dropout (S=30)
Temp. Scaling (T=2.70)
ECE: 0.265→0.048 KS: 0.245→0.104
Single parameter No retraining
Gaussian assumption Residual miscal. at tails
Temp. Scaling (T=2.70)
Standard Conformal
PICP 90%: 90.02% PICP 95%: 95.01%
Coverage guarantee Distribution-free
Fixed-width intervals Poor conditional coverage
Standard Conformal
Adaptive Conformal
Cond. cov. [90.0%, 96.2%]
Node-specific widths Conditional coverage
Requires σ from MC Dropout
Adaptive Conformal
Multi-Model Ensemble
ρ=0.4333 R²=0.5656
Complementary signal No MC overhead
Weaker than MC Dropout No accuracy gain over T8 alone
Multi-Model Ensemble

## Slide 24
Traffic Context: What is Being Predicted?
Δv = change in traffic volume per road segment after policy intervention
24
Technical University of Munich | Chair of Urban Transport Systems
24
Fig: 19. Distribution of 5 input features across 200 training graphs (6.33M node observations). VOL_BASE_CASE and CAPACITY_BASE_CASE are right-skewed (heavy-tailed urban traffic). FREESPEED shows discrete speed limits. LENGTH spans several orders of magnitude.
What is Δv?
The change in traffic volume on each
road segment after a policy applies:
Δv = v_policy − v_baseline (veh/h)
Policy = capacity reduction:
• 10%–100% of road capacity reduced
• Applied to a random subset of roads
• Simulates: lane closures, traffic calming,
bus-only lanes, congestion pricing...
Why hard to predict?
• Traffic redistributes across network
• High-flow roads change most but vary most
• ρ ≈ 0.74–0.81 (low-flow) vs 0.26–0.41 (high-flow)

## Slide 25
Traffic Policy: 3-Tier Decision Framework
Uncertainty-guided workflow for urban planners
25
Technical University of Munich | Chair of Urban Transport Systems
25
Fig: 20. Uncertainty-guided decision framework. GNN surrogate (T8, S=30) routes each prediction based on MC Dropout σ. Bottom 50% = ACCEPT, 50–90% = FLAG, Top 10% = REJECT for re-simulation.
ACCEPT
Bottom 50% of σ
MAE ≈ 2.32 veh/h −41.2% error
Use surrogate output directly for policy decision
FLAG
50th–90th percentile
Some uncertainty present
Sensitivity analysis or cross-check needed
REJECT
Top 10% of σ
High uncertainty run full MATSim
Route to full 8-hr MATSim simulation

## Slide 26
Impact for Urban Planning
How this thesis changes the policy evaluation workflow
26
Technical University of Munich | Chair of Urban Transport Systems
26
Fig: 21. ROC curves for T8 MC Dropout as error detector. AUROC=0.76 (top-10% errors) and 0.74 (top-20% errors) — well above 0.5 random baseline. Model can identify unreliable predictions before a planner acts on them.
Faster policy screening
Seconds per scenario instead of 8+ hours. Hundreds of alternatives evaluated in hours.
Reliable uncertainty scores
ρ=0.4820: high-σ roads reliably indicate where model may be wrong. AUROC=0.76 for flagging top-10% errors.
Smart resource allocation
Expensive MATSim re-simulation only for top-10% uncertain predictions. 90% of predictions can be accepted or flagged.
Statistically valid intervals
Conformal prediction gives ±14.68 veh/h interval with 95% coverage guarantee — suitable for formal planning documents.

## Slide 27
Summary: Answers to All 4 Research Questions
27
Technical University of Munich | Chair of Urban Transport Systems
27
RQ1
MC Dropout Effectiveness
T8 achieves Spearman ρ = 0.4820 (100 test graphs, 3.16M predictions). Consistent per-graph ρ = 0.464 ± 0.023. AUROC = 0.76 for top-10% error detection. Enabling dropout costs only ΔR² = −0.010.
RQ2
MC Dropout vs Ensembles
MC Dropout (ρ=0.4908) outperforms ensemble variance (ρ=0.4370) by +12.3% and multi-model disagreement (ρ=0.4333) by +13.3%. MC Dropout is best and most computationally efficient single method.
RQ3
Combining Identical Models
Combined MC+Ensemble (ρ=0.4909) barely beats MC alone (ρ=0.4908): negligible gain. Multi-model ensemble R²=0.5656 < best single T8 R²=0.5957. Architectural diversity not tested — may unlock further benefits.
RQ4
Distribution-Free Coverage
Yes. Conformal: 90.02% @ 90%, 95.01% @ 95% — guaranteed. Temperature scaling reduces ECE by 82%. Adaptive conformal narrows conditional coverage from [62.9%,98.6%] to [90%,96.2%].

## Slide 28
Limitations
Honest assessment of what this thesis does NOT show
28
Technical University of Munich | Chair of Urban Transport Systems
28
10% Data Subset
Only 1,000 of 10,000 available scenarios used. Natterer et al. achieved R²=0.91 with full dataset. Gap from R²=0.60 likely due to 10× less training data.
Single Road Network
All experiments on Paris only. Generalisation to other cities, topologies, or policy types not tested. Feature correlation patterns may differ elsewhere.
Identical Architecture Ensembles
Ensemble experiments use only PointNetTransfGAT variants. True architectural diversity (GAT + GraphSAGE + GCN) not tested — may unlock further UQ benefits.
Epistemic Only
MC Dropout captures only epistemic (model) uncertainty. Aleatoric (data/noise) uncertainty not separated. T9 heteroscedastic attempt failed (R²=0.02 — variance inflation).
No Non-GNN Baselines
No comparison to random forests, GPs, or MLP ensembles. Unclear if ρ=0.4820 is specific to GNN or achievable by simpler models.

## Slide 29
Future Work
Six directions for extending this research
29
Technical University of Munich | Chair of Urban Transport Systems
29
Full 10k Scenarios
Train on complete 10,000-scenario dataset. Assess if R² and ρ scale with more data.
Architecturally Diverse Ensembles
Combine GAT + GraphSAGE + GCN models. True diversity may improve UQ beyond ρ=0.4333.
Conformal Risk Control
Extend to arbitrary loss functions. Tighter adaptive intervals via conformal risk control.
Epistemic-Aleatoric Decomposition
Evidential deep learning approach. Separate model uncertainty from data noise.
Multi-City Validation
Test on London, Berlin, Munich networks. Check generalisability of UQ findings.
Active Learning
Use high-σ predictions to select new MATSim scenarios for training.

## Slide 30
Conclusion
ML Surrogates for Agent-Based Transport Models
1
MC Dropout works.
ρ=0.4820 on 3.16M predictions. Useful ranking signal with AUROC=0.76. Cost to enable: ΔR²=−0.010 (negligible).
2
Conformal prediction delivers guarantees.
90.02% and 95.01% coverage achieved by construction. Adaptive variant reduces conditional disparity from [62.9%,98.6%] to [90%,96.2%].
3
Use the 3-layer hierarchy in practice.
MC Dropout for ranking → temperature scaling for calibration → conformal prediction for formal guarantees. All post-hoc, no retraining.
Thank you | Questions welcome